## Slide 1
Enabling ISAC on the OAI nrUE
Integrated Sensing & Communication via LPP, PRS and the T-tracer
Design overview — the nrUE as a joint sensing device and communication terminal
Today in OAI (baseline)
• LPP (TS 37.355) exists as ASN.1 grammar only (openair3/LPP, Rel-16 g60) — compiled but not linked; no UE positioning entity.
• nrUE PRS reception computes per-antenna DL ToA, RSRP and SNR (nr_prs_channel_estimation).
• CFO is estimated (PSS/PBCH) for compensation only; dl_aoa is a placeholder; per-antenna CIR is discarded.
• Positioning stack (NRPPa / F1AP) lives on the gNB side, not the UE.
ISAC target (this work)
• UL/DL AoA, AoD & Doppler derived at PHY and exported for sensing via the T-tracer.
• PRS reused as the sensing waveform — CIR → range / angle / Doppler.
• GPS & UE location / assistance delivered over LPP (A-GNSS, NR-DL-AoD, Multi-RTT, DL-TDOA).
• One nrUE = communication + sensing on the same PRS/SRS signalling.
Scope grounded in the OAI codebase and 3GPP Rel-16/17 ISAC & LPP concepts.

## Slide 2
How AoA / AoD / Doppler & GPS are obtained
PRS/SRS → PHY observables → T-tracer export (sensing) | measurements + GPS → LPP (communication / positioning)
1 . PRS → range & angle
2 . Doppler / velocity
3 . GPS time & UE location
• DL: PRS channel estimate → CIR (IDFT). Peak = ToA / range.
• Per-Rx-antenna complex CIR already computed → inter-antenna phase gives DL-AoA / AoD (to add).
• UL: gNB SRS → ToA & UL-AoA (NRPPa / F1AP positioning).
• Also available: RSRP, SNR per antenna for detection gating.
• CFO estimated at sync (PSS fractional + PBCH fine), stored as freq_offset.
• Phase drift of PRS CIR across occasions → Doppler shift → radial velocity.
• freq↔velocity math already in NTN path (dl_Doppler_shift).
• Coherent integration over PRS occasions → range–Doppler map (to add).
• GPSDO on the RF front-end gives absolute GPS/TAI time + 1-PPS (sync_to_gps).
• Timestamps every sensing measurement; aligns multi-gNB PRS.
• UE geodetic location & assistance via LPP A-GNSS (assistance data + navigation model).
• LPP ProvideLocationInformation carries NR-DL-AoD / Multi-RTT / DL-TDOA + Velocity.
SENSING export — T-tracer
• New event in T_messages.txt, e.g. T_UE_PHY_SENSING : frame:slot:aoa:aod:doppler:toa:rsrp.
• Emitted with the T(…) macro at the PRS chest site (as existing T_UE_PHY_DL_CHANNEL_ESTIMATE).
• Collected live by record / textlog / extract → offline range–Doppler / angle processing.
COMMUNICATION / positioning export — LPP
• New UE LPP entity links the existing asn1_lpp codec (37355-g60).
• Transports LPP transparently over NAS/RRC to the LMF.
• Capabilities → Assistance → ProvideLocationInformation with the measured AoA/AoD/ToA/Doppler + GNSS.

## Slide 3
nrUE as a joint sensing + communication node
One PHY, two outputs: sensing observables (T-tracer) and positioning/comms (LPP to LMF)
gNB / TRP
DL PRS / UL SRS
Object /
target
OAI nrUE — PHY
PRS channel est. → CIR
ToA / RSRP / SNR
per-antenna CIR (AoA/AoD)
CFO → Doppler
GPSDO: GPS/TAI time + 1-PPS
T-tracer
T_UE_PHY_SENSING
SENSING
range · AoA/AoD · Doppler
range–Doppler map
LPP entity
(asn1_lpp / TS 37.355)
LMF
position fix +
communication
transparent over NAS / RRC
echo
sensing
positioning
Status
✓ Exists today: PRS ToA/RSRP/SNR, per-antenna CIR, CFO, LPP ASN.1, GPSDO time, T-tracer.
▸ To add for ISAC: AoA/AoD & Doppler estimators, sensing T-event, UE LPP entity + NAS/RRC transport.
Legend
■ sensing data path — T-tracer (range, AoA/AoD, Doppler).
■ communication / positioning path — LPP, GPS.
■ PRS (DL) / SRS (UL) radio link.